# Introduction
The aim of this document is to derive the equations behind the Qucs attenuator synthesis tool in what concerns power dissipation in the resistors. Sinusoidal steady state regime is assumed:
For every node and every branch, voltages and currents are defined as follows:
Instantaneouts voltage: v(t) = V_{0}· sin(%omega · t)
Instantaneouts current: i(t) = I_{0}· sin(%omega · t + %phi)
Since the attenuators here are purely resistive, so %phi = 0 .
The instantaneous power is given by the product of the voltage and current waves:
p(t) = v(t)·i(t) = V_{0} · I_{0} · sin(%omega · t) · sin( %omega · t - %phi ) = V_{ 0 } · I_{ 0 } · (cos(%phi) · sin^2(%omega · t) - sin(%phi) · sin (%omega · t) · cos(%omega · t))
p(t) = V_{ 0 } · I_{ 0 } · sin^2( %omega · t )
Thus, the average power:
P_{ avg } = {V_{ 0 } · I_{ 0 }} over T · int_0^T sin^2( %omega · t) = V_{ 0 } · I_{ 0 }
where T is the wave period.
In the following, PRi will denote the average power dissipated by Ri:
P_{"in"} = {V_{"in"}^2} over {Z_{"in"}} = I_{"in" }^2 · Z_{ "in" } drarrow V_{ "in" } = sqrt{P_{"in"}·Z_{"in"}}, I_{"in"} = sqrt{P_{"in"} over Z_{"in"}}
The input and output impedances ( Z_{ "in" } and Z_{ "out" } respectively) of the attenuator are real and not necessarily equal.

In what follows, Octave was used for plotting and SAGE and WolframAlpha for the simplification large expressions.

# π attenuator
## Design equations
The schematic and the design equations of the pi attenuator are detailed as follows [1].
R_{ 1 } = 1 over { {{10^{0.1 · att} + 1} over {Z_{"in"} · (10^{0.1 · att}-1)}} - {1 over R_{2}} }
R_{ 2 } = 0.5 · ( 10^{0.1 · att} - 1 ) · sqrt{ {Z_{"in"} · Z_{"out"}} over {10^{0.1 · att}} }
R_{ 3 } = 1 over{ {{10^{0.1 · att} + 1} over {Z_{"out"} · (10^{0.1 · att} -1)}} - {1 over R_{2}} }

## Power dissipation

Power dissipated by R1:
P_{ R1 } = V_{1}^2 over {R_{1}}, V_{1} = V_{ "in" }, V_{"in"} = sqrt{P_{"in"}·Z_{"in"}} drarrow P_{ R1 } = { P_{"in"} · Z_{"in"}} over {R_{1}}
P_{ R1 } over P_{ "in" } = Z_{ "in" } over R_{ 1 }

Power dissipated by R2:
P_{R2} = I_{2 }^2 · {R_{2}}, I_{2} = I_{"in"} - I_{ 1 } I_{ 1 } = V_{1} over R_{ 1 } = sqrt{P_{"in"} · Z_{"in"}} over R_{1 } drarrow I_{2 } = sqrt{P_{"in"} over Z_{"in"}} - { sqrt{P_{"in"} · Z_{"in"}} over R_{1}}
P_{R2} = left ( sqrt{P_{"in"} over Z_{"in"}} - { sqrt{P_{"in"} · Z_{"in"}} over R_{1}} right ) ^2 · R_{2} = P_{"in" } · R_{ 2 } · left ( sqrt{1 over Z_{"in"}} - { sqrt{ Z_{"in"}} over R_{1}} right )^2
P_{R2} over P_{"in"} = {R_{ 2 } · (R_{1}-Z_{"in"})^2 } over { R_{1}^2 · Z_{"in"}}

Power dissipated by R3:
P_{ R3 } = V_{ "out" }^2 over R_{3}, V_{ out } = V_{ "in" } - I_{ 2 }·R_{ 2 }
P_{ R3 } = left ( sqrt{P_{"in"} · Z_{"in"}} - left ( sqrt{P_{"in"} over Z_{"in"}} - sqrt{P_{"in"} · Z_{"in"}} over R_{1} right ) · R_{2} right )^2 over R_{3 } = {P_{"in"} over R_{3}} · left ({ sqrt{Z_{"in"}} - left ( sqrt{1 over Z_{"in"}} - sqrt{Z_{"in"}} over R_{1} right ) · R_{2} } right )^2
P_{ R3 } over P_{"in"} = { (R_{1} · R_{2} - Z_{"in"} · (R_{1} + R_{2}))^2 } over { R_{1}^2 · R_{3} · Z_{"in"} }

Finally, the output power, Pout, can be calculated as follows:
P_{ "out" } = V_{ "out" }^2 over Z_{"out"}, V_{ out } = V_{ "in" } - I_{ 2 }·R_{ 2 }
P_{ "out" } = left ( sqrt{P_{"in"} · Z_{"in"}} - left ( sqrt{P_{"in"} over Z_{"in"}} - sqrt{P_{"in"} · Z_{"in"}} over R_{1} right ) · R_{2} right )^2 over Z_{"out" } = {P_{"in"} over Z_{"out"}} · left ({ sqrt{Z_{"in"}} - left ( sqrt{1 over Z_{"in"}} - sqrt{Z_{"in"}} over R_{1} right ) · R_{2} } right )^2
And now, the attenuation may be expressed in terms of the resistor values and the input/output impedances:
P_{ "out" } over P_{"in"} = { (R_{1} · R_{2} - Z_{"in"} · (R_{1} + R_{2}))^2 } over { R_{1}^2 · Z_{"out"} · Z_{"in"} }

Since attenuation is commonly expressed in dB units:
%alpha = 10·log_{ 10 } left( P_{ "out" } over P_{"in"} right ) = 10·log_{ 10 } left( { (R_{1} · R_{2} - Z_{"in"} · (R_{1} + R_{2}))^2 } over { R_{1}^2 · Z_{"out"} · Z_{"in"} } right )

%alpha = 20·log_{ 10 } left( { R_{1} · R_{2} - Z_{"in"} · (R_{1} + R_{2}) } over { R_{1} · sqrt{Z_{"out"} · Z_{"in"}} } right)
# Tee attenuator
## Design equations

The schematic and the design equations of the pi attenuator are detailed as follows [1].
R_{ 1 } = { {10^{0.1 · att} + 1} over {10^{0.1 · att} - 1} } · Z_{ "in" } - R_{ 2 }
R_{ 2 } = { 2 · sqrt{Z_{"in"} · Z_{"out"} · 10^{0.1 · att} }} over { 10^{0.1 · att} -1}
R_{ 3 } = { {10^{0.1 · att} + 1} over {10^{0.1 · att} - 1} } · Z_{ "out" } - R_{ 2 }

## Power dissipation

Power dissipated by R1:
P_{ R1 } = I_{ 1 }^2 · R_{ 1 } = { P_{"in"} · R_{1} } over Z_{ "in" }
P_{ R1 } over P_{"in"}= R_{1} over Z_{ "in" }

Power dissipated by R2:
P_{ R2 } = V_{ 1 }^2 over R_{ 2 }, V_{ 1 } = V_{"in"} - I_{1} · R_{1} drarrow P_{ R2 } = left ( V_{"in"} - I_{1} · R_{1} right)^2 over R_{ 2 } = left ( sqrt{P_{"in"} · Z_{"in"}} - sqrt{P_{"in"} over Z_{"in"}} · R_{1} right)^2 over R_{ 2 }
P_{ R2 } over P_{ "in" } = left( { sqrt{Z_{"in"}} - {R_{1} over sqrt{Z_{"in"}} }} right)^2 over R_{ 2 }
P_{ R2 } over P_{ "in" } = ( R_{1}-Z_{"in"} )^2 over { R_{2} · Z_{"in"} }

Power dissipated by R3:
P_{ R3 } = I_{ 3 }^2 · R_{ 3 }
I_{ 3 } =I_{ 1 } - I_{ 2 } = sqrt{P_{"in"} over Z_{"in"}} - V_{ 1 } over R_{ 2 } = sqrt{P_{"in"} over Z_{"in"}} - {sqrt{P_{"in"} · Z_{"in"}} - sqrt{P_{"in"} over Z_{"in"}} · R_{1}} over R_{ 2 }
P_{ R3 } = left( sqrt{P_{"in"} over Z_{"in"}} - {sqrt{P_{"in"} · Z_{"in"}} - sqrt{P_{"in"} over Z_{"in"}} · R_{1}} over R_{ 2 } right )^2 · R_{ 3 } drarrow P_{ R3 } over P_{ "in" } = left( 1 over sqrt{Z_{"in"}} - {sqrt{Z_{"in"}} - R_{1} over sqrt{Z_{"in"}}} over R_{2} right)^2 · R_{ 3 }
P_{ R3 } over P_{ "in" } = { R_{3} · (R_{1} + R_{2} - Z_{"in"})^2 } over {Z_{"in"} ·R_{2}^2}

# Comparison between the Pi and Tee type resistive attenuators

	Pi	Tee
R1	P_{ R1 } over P_{ "in" } = Z_{ "in" } over R_{ 1 }	P_{ R1 } over P_{"in"}= R_{1} over Z_{ "in" }
R2	P_{R2} over P_{"in"} = {R_{ 2 } · (R_{1}-Z_{"in"})^2 } over { R_{1}^2 · Z_{"in"}}	P_{ R2 } over P_{ "in" } = ( R_{1}-Z_{"in"} )^2 over { R_{2} · Z_{"in"} }
R3	P_{ R3 } over P_{"in"} ={ ({R_{1} · R_{2} - Z_{"in"}·(R_{1} + R_{2})})^2 over {R_{1}^2 · R_{3} · Z_{"in"}} }	P_{ R3 } over P_{ "in" } = { R_{3} · (R_{1} + R_{2} - Z_{"in"})^2 } over {Z_{"in"} ·R_{2}^2}

If Z_{"in"} = Z_{ "out" } drarrow R_{ 1 } = R_{ 3 } :

	Pi	Tee
R1	P_{ R1 } over P_{ "in" } = Z_{ "in" } over R_{ 1 }	P_{ R1 } over P_{"in"}= R_{1} over Z_{ "in" }
R2	P_{R2} over P_{"in"} = {R_{ 2 } · (R_{1}-Z_{"in"})^2 } over { R_{1}^2 · Z_{"in"}}	P_{ R2 } over P_{ "in" } = ( R_{1}-Z_{"in"} )^2 over { R_{2} · Z_{"in"} }
R3	P_{ R3 } over P_{"in"} ={ {R_{1} · (Z_{"in"} - R_{2}) + Z_{"in"} · R_{2}} over {R_{1}^3 · Z_{"in"}} }	P_{ R3 } over P_{ "in" } = { R_{1} · (R_{1} + R_{2} - Z_{"in"})^2 } over {Z_{"in"} ·R_{2}^2}

and the power dissipated in each resistor is the same both the Pi and Tee configuration.

Illustration 1: Relative power dissipation for each resistor (Zin = Zout=50Ω)

Illustration 2: Relative power dissipation for each resistor (Zin = 50Ω, Zout = 75Ω)

The minimum attenuation that a Pi or Tee attenuation can achieve depends on the ratio of the input and output impedance according to the following expression [1]:
L_{ "min" } = 20 · log_{ 10 } ( sqrt{{Z_{"in"} over {Z_{"out"}}}} + sqrt{{Z_{"in"}}over{Z_{"out"}}-1})

Illustration 3: Minimum attenuation loss vs Zin/Zout

# Bridged Tee
## Design equations
The bridged Tee attenuator requires Z_{ "in" } = Z_{ "out" }
R_{ 1 } = Z_{ 0 } · ( 10^{0.05 · att} - 1) R_{ 4 } = Z_{ 0 } over { 10^{0.05 · att} - 1 }
## Power dissipation

I_{ 1 } = {V_{ "in" } - V_{ "out" }} over R_{ 1 } I_{ 2 } = { V_{"in"} - V_{4} } over R_{ 2 } I_{ 3 } = { V_{"out"} - V_{4} } over R_{ 3 } I_{ 4 } = V_{ 4 } over R_{ 4 }
R1	P_{R1} over {P_{"in"}} = { 4·R_{1}·R_{4}^2·Z_{0} } over { (R_{1}· R_{4} + Z_{0}·(2·R_{4}+Z_{0}))^2 }
R2	P_{R2} over {P_{"in"}} = { (R_{1}·R_{4} + Z_{0}^2)^2 } over { (R_{1}·R_{4} + Z_{0}·(2·R_{4}+Z_{0}))^2 }
R3	P_{R3} over {P_{"in"}} = 0
R4	P_{R4} over {P_{"in"}} = { 4·R_{4}·Z_{0}^3 } over { (R_{1}·R_{4} + Z_{0}·(2·R_{4}+Z_{0}))^2 }

Illustration 4: Relative power per resistence (Z0 = 50Ω)

Most of the power is dissipated in R2, whose value is constant. In variable attenuators R2 and R3 are standard SMD resistor whereas R1 and R4 are PIN diodes. Notice that R1 and R4 dissipate little power, so this is convenient for minimizing distortion.

# Reflection attenuator

## Design equations

S_{21} = S_{31} · (-S_{33}) · S_{23} + S_{ 41 } · (-S_{44}) · S_{24}= left ( {Z_{0} - R_{i}} over {Z_{0} - R_{i}} right ) · (S_{31}·S_{23} + S_{41}·S_{24} ) = left ( {Z_{0} - R_{i}} over {Z_{0} - R_{i}} right ) · left( {1 over sqrt{2}} · {e^{j%pi/2} over sqrt{2}} + {e^{j%pi/2} over sqrt{2}} · {1 over sqrt{2}} right)
S_{ 21 } = left( {Z_{0} - R_{i}} over {Z_{0} + R_{i}} right ) · e^{ j%pi/2 }
%alpha = -20·log_{10}( abs{S_{21}} ) = -20 · log_{ 10 } left( abs{{Z_{0} - R_{i}} over {Z_{0} + R_{i}}} right )
10^{ -0.05 · %alpha } = abs{{Z_{0} - R_{i}} over {Z_{0} + R_{i}}} dlrarrow ( Z_{0} + R_{i} ) · 10^{ -0.05 · %alpha } = abs{Z_{0} - R_{i}}
if R_{ i } < Z_{ 0 }
R_{ i } = -Z_{ 0 } · ( 10^{-0.05 · %alpha} - 1) over {(1 + 10^{-0.05 · %alpha}) } = Z_{ 0 } · ( 1 - 10^{-0.05 · %alpha} ) over {(1 + 10^{-0.05 · %alpha} )}
if R_{ i } > Z_{ 0 }
R_{ i } = Z_{ 0 } · ( 1 + 10^{-0.05 · %alpha}) over {(1 - 10^{-0.05 · %alpha}) }
## Power dissipation
The power dissipated in the resistors is the difference between the incident power and the reflected one.
The incident power in the both resistors is given by:
P_{ "inc" }= P_{ "in" } · {abs{S_{ i1 }}}^2
P_{ "refl" } = P_{ "in" } · {abs{S_{ii}}}^2
P_{ "diss" } = P_{ "inc" }^{ R_{3} } - P_{ "refl" }^{ R_{3} } = P_{"in"} · {abs{S_{ i1}}}^2 · ( 1 - {abs{S_{ii}}}^{2} )
where
S_{ "ii" } = {Z_{ 0 } - R_{ i } } over { Z_{ 0 } + R_{ i } }
abs{S_{ "i1" }} = 1 over sqrt{ 2 }
P_{ "diss" } = {P_{"in"} over 2} · left ( 1 - {abs{ {Z_{ 0 } - R_{ "i" } } over { Z_{ 0 } + R_{ "i" } }}}^2 right )

if R_{ i } < Z_{ 0 }
P_{ "diss" } = {P_{"in"} over 2} · left ( 1 - {abs{ {Z_{ 0 } - {Z_{ 0 } · ( 1 - 10^{-0.05 · %alpha} ) over {(1 + 10^{-0.05 · %alpha} )}} } over { Z_{ 0 } + {Z_{ 0 } · ( 1 - 10^{-0.05 · %alpha} ) over {(1 + 10^{-0.05 · %alpha} )}} }}}^2 right ) = {P_{"in"} over 2} · left ( 1 - {abs{ {1 - {( 1 - 10^{-0.05 · %alpha} ) over {(1 + 10^{-0.05 · %alpha} )}} } over { 1 + {( 1 - 10^{-0.05 · %alpha} ) over {(1 + 10^{-0.05 · %alpha} )}} }}}^2 right )
P_{ "diss" } = {P_{"in"} over 2} · left ( 1 - {abs{ {{{(1 + 10^{-0.05 · %alpha} ) - ( 1 - 10^{-0.05 · %alpha} )} over {(1 + 10^{-0.05 · %alpha} )}} } over {{ {(1 + 10^{-0.05 · %alpha} ) + ( 1 - 10^{-0.05 · %alpha} )} over {(1 + 10^{-0.05 · %alpha} )}} }}}^2 right ) = {P_{ "in" } over 2} · left( 1 - {abs{{(1 + 10^{-0.05 · %alpha} ) - ( 1 - 10^{-0.05 · %alpha} )} over{(1 + 10^{-0.05 · %alpha} ) + ( 1 - 10^{-0.05 · %alpha} )}}}^2right )
P_{ "diss" } = { P_{"in"} over 2 } · left( 1 - {abs{{2·10^{-0.05·%alpha}} over {2}}}^2 right ) = { P_{"in"} over 2 } · left( 1 - {10^{-0.1·%alpha}} right )

if R_{ i } > Z_{ 0 }
P_{ "diss" } = {P_{"in"} over 2} · left ( 1 - {abs{ {Z_{ 0 } - Z_{ 0 } · ( 1 + 10^{-0.05 · %alpha}) over {(1 - 10^{-0.05 · %alpha}) } } over { Z_{ 0 } + Z_{ 0 } · ( 1 + 10^{-0.05 · %alpha}) over {(1 - 10^{-0.05 · %alpha}) } }}}^2 right ) = {P_{"in"} over 2} · left ( 1 - {abs{ {1 - ( 1 + 10^{-0.05 · %alpha}) over {(1 - 10^{-0.05 · %alpha}) } } over { 1 + ( 1 + 10^{-0.05 · %alpha}) over {(1 - 10^{-0.05 · %alpha}) } }}}^2 right )
P_{ "diss" } = {P_{"in"} over 2} · left ( 1 - {abs{ {{{(1 - 10^{-0.05 · %alpha} ) - ( 1 + 10^{-0.05 · %alpha} )} over {(1 - 10^{-0.05 · %alpha} )}} } over {{ {(1 - 10^{-0.05 · %alpha} ) + ( 1 + 10^{-0.05 · %alpha} )} over {(1 - 10^{-0.05 · %alpha} )}} }}}^2 right ) = {P_{ "in" } over 2} · left( 1 - {abs{{(1 - 10^{-0.05 · %alpha} ) - ( 1 + 10^{-0.05 · %alpha} )} over{(1 - 10^{-0.05 · %alpha} ) + ( 1 + 10^{-0.05 · %alpha} )}}}^2right )
P_{ "diss" } = { P_{"in"} over 2 } · left( 1 - {abs{{-2·10^{-0.05·%alpha}} over {2}}}^2 right )
Thus, the power dissipated by the resistors is the same regardless R_{ i } < Z_{ 0 } or R_{ i } > Z_{ 0 } .

# Quarter-wave series attenuator

## Design equations
Y_{1} = left[matrix{1#0## {1 over {R+Z_{0}}} # 1}right]
A_{TL} = left[matrix{cosh(%gamma · l)#Z_{0} · sinh(%gamma · l)## {1 over {Z_{0}}}· sinh(%gamma · l) # cosh(%gamma · l)}right]
where %gamma = %alpha + j·%beta is the propagation constant. Since the λ/4-transmission line is supposed to be lossless, then %gamma = j·%beta = j · { 2 · %pi } over { %lambda } and, consequently:
A_{TL} = left[matrix{0#j·Z_{0}## {j over {Z_{0}}} # 0}right]
Y_{2} = left[matrix{1#0## {1 over {R}} # 1}right]

The overall ABCD matrix is given by:
A_{QW} = Y_{ 1 } · A_{ TL } · Y_{ 2 } = left[matrix{{{j·Z_{0}} over {R}}#j·Z_{0}## {j over {Z_{0}}} + {j·Z_{0}} over {R·(R+Z_{0})} # {j·Z_{0}} over {R+Z_{0}}}right] = j · Z_{0} · left[matrix{{{1} over {R}}#1## {left( {{1} over {R·(R+Z_{0})}} + {1 over {Z_{0}}^2}right)} # {1} over {R+Z_{0}}}right]
Using the conversion formulae between ABCD and S parameters:
S = left[matrix{0#-j · { R } over { R + Z_{0} }## -j · { R } over { R + Z_{0} } # { {Z_{0}}^2 } over { (R + Z_{0})^2 }}right]
Thus, the attenuation can be expressed in terms of R and Z0 as follows:
%alpha = -10 · log_{ 10 } left ( abs{S_{21}}^2 right ) = -20·log_{ 10 } left( {R} over {R+Z_{0}} right )
{ R } over { R+Z_{0} } = 10^{ -%alpha over 20 } drarrow R = { Z_{0} · 10^{-%alpha over 20} } over { 1 - 10^{-%alpha over 20} } = { Z_{0} } over { 10^{%alpha over 20} - 1 }
R = { Z_{0} } over { 10^{%alpha over 20} - 1 }

The impedance inversion property of the λ/4-transmission line holds for narrowband applications. The general (broadband) expressions for the S-parameters are rather complex, so numeric S-parameter simulation is preferred.
The impedance seen at the output port is given by:
Z_{ out } = left(Z_0^2 over (Z_0 parallel Z_1) parallel R right) = left(Z_0^2 over (Z_0 parallel Z_1) parallel R right) = ( R^2 · Z_0 + 2·R·Z_0^2 ) over ( R^2 + 2 · R · Z_0 + 2 · Z_0^2 )

Illustration 5: Frequency response of a 10dB Quarter Waver series attenuator.
## Power dissipation at f0
P_{ R1 } = I_{ 1 }^2 · R_{ 1 } = left( {V_{"in"}} over {R_{1} + Z_{0}} right )^2 · R_{1} = I_{ 1 }^2 · R_{ 1 } = left( {sqrt{P_{"in"}·Z_{0}}} over {R_{1} + Z_{0}} right )^2 · R_{1}= left( {P_{"in"} · Z_{0}} over {(R_{1} + Z_{0})^2} right ) · R_{1}
P_{ R1 } = left( {P_{"in"} · Z_{0}} over {(R_{1} + Z_{0})^2} right ) · R_{1}

P_{ R2 } = left( {P_{"in"} · {Z_{0}}^2} over {(R_{1} + Z_{0})^2} right )

P_{ 2 } = P_{ "in" } - ( P_{R1} + P_{R2}) = P_{ "in" } - left( left( {P_{"in"} · Z_{0}} over {(R_{1} + Z_{0})^2} right ) · (R_{1} + Z_{0}) right) = P_{ "in" } left( 1 - left( {Z_{0} · (R_{1} + Z_{0})} over {(R_{1} + Z_{0})^2} right) right)
V_{ "out" } = sqrt{P_{2} · left( {R_{3} · Z_{0}} over {R_{3} + Z_{0}} right)} = sqrt{P_{ "in" } left( 1 - left( {Z_{0} · (R_{1} + Z_{0})} over {(R_{1} + Z_{0})^2} right) right) · left( {R_{3} · Z_{0}} over {R_{3} + Z_{0}} right)}
Thus, the power dissipated by R3 is given by:
P_{ R3 } = { {V_{"out"}}^2 } over { R_{3} } = { P_{ "in" } left( 1 - left( {Z_{0} · (R_{1} + Z_{0})} over {(R_{1} + Z_{0})^2} right) right) · left( {R_{3} · Z_{0}} over {R_{3} + Z_{0}} right) } over { R_{3} }
And, finally, the power delivered to the load:
P_{ "out" } = { {V_{"out"}}^2 } over { Z_{0} } = { P_{ "in" } left( 1 - left( {Z_{0} · (R_{1} + Z_{0})} over {(R_{1} + Z_{0})^2} right) right) · left( {R_{3} · Z_{0}} over {R_{3} + Z_{0}} right) } over { Z_{0} }
Since R_{ 1 } = R_{ 3 } = R PR3 and Pout admit further simplification:
P_{ R3 } = P_{ R1 } = P_{"in"}·{ R · Z_{0} } over { (R + Z_{0})^2 }

P_{ "out" } = P_{"in"}·{ R^2 } over { (R + Z_{0})^2 }

Sanity check:
%alpha = 10 · log_{10} left( {P_{"out"}}over{P_{"in"}}right) = 10·log_{10} left({ R^2 } over { (R + Z_{0})^2 } right) = 20 · log_{ 10 } left( { R } over { (R + Z_{0}) }right ) which is the same expression we found in 7.1

As seen in the previous graph, R2 dissipates much more power than the other resistors. Since R2 does not depend on the attenuation, this structure may be particularly interesting in order to implement PIN based variable attenuators.
# Quarter-wave shunt attenuator

## Design equations
At f0, the λ/4 line behaves as an impedance inverter such as its input impedance is given by:
Z_{ "TL" } = Z_{ 0 }^2 over Z_{ L }, Z_{ L } = { R · Z_{0} } over { R + Z_{0} } drarrow Z_{ "TL" } = { Z_{0} · (R + Z_{0}) } over { R}
So the ABCD parameters of the shunt branch are:
Y_{1} = left[matrix{1#0## {R over {Z_{0}·(R +Z_{0})}} # 1}right]
The ABCD parameters of the series resistor is given by: A_{2} = left[matrix{1#R## 0 # 1}right]
Therefore, the ABCD parameters of the quarter-wave shunt attenuator can be expressed as the product of the previous matrices:
ABCD = Y_{ 1 } · A_{ 2 } = left[matrix{1#R## {R over{(R + Z_{0})·Z_{0}}} # {R^2} over {(R + Z_{0})·Z_{0}} + 1}right]
Using the conversion formulae between ABCD and S parameters:
S = left[matrix{0# { Z_{0} } over { R + Z_{0} }## { Z_{0} } over { R + Z_{0} } # { {R}^2 } over { (R + Z_{0})^2 }}right]
Thus, the attenuation can be expressed in terms of R and Z0 as follows:
%alpha = -10 · log_{ 10 } left ( abs{S_{21}}^2 right ) = -20·log_{ 10 } left( {Z_{0}} over {R+Z_{0}} right )
{ Z_{0} } over { R+Z_{0} } = 10^{ -%alpha over 20 } dlrarrow Z_{ 0 } = R · 10^{ -%alpha over 20 } + Z_{ 0 } · 10^{ -%alpha over 20 } drarrow R = Z_{ 0 } · (1 - 10^{ -%alpha over 20 }) over 10^{ -%alpha over 20 } = Z_{ 0 } · (1 - 10^{ -%alpha over 20 }) · 10^{ %alpha over 20 } = Z_{ 0 } · ( 10^{ %alpha over 20 } -1 )
R = Z_{ 0 } · ( 10^{ %alpha over 20 } -1 )

The output impedance is given by:
Z_{ out } = R + Z_1 parallel Z_0 = R + { Z_0 · (R + Z_0) } over { 2 · R + Z_0 }
## Power dissipation
The power dissipated by the shunt branch is given is:
P_{ "shunt" } = V_{ "in" }^2 over Z_{ "TL" } = P_{"in"}· R over { R + Z_{0} }
and consequently V1 may be expressed as:
V_{ 1 } = sqrt{ P_{"shunt"} · R_{"eq"} } = sqrt{ P_{"shunt"} · left( {R·Z_{0}} over {R + Z_{0}} right) } = sqrt{ P_{"in"}·{R over {R+Z_{0}}} · left( {R·Z_{0}} over {R + Z_{0}} right) } ={R· sqrt{P_{"in"}· Z_{0}}} over {R + Z_{0}}
so the power dissipated by R2 and R3 is given by:
P_{ R2 } = V_{ 1 }^2 over Z_{ 0 } = { left( {R· sqrt{P_{"in"}· Z_{0}}} over {R + Z_{0}} right)^2 } over Z_{ 0 } = P_{"in"}· { R^2 } over { (R+Z_{0})^2 }
P_{ R3 } = V_{ 1 }^2 over R = { left( {R· sqrt{P_{"in"}· Z_{0}}} over {R + Z_{0}} right)^2 } over R = P_{"in"}· { R · Z_0 } over { (R+Z_{0})^2 }
The mean current which flows through the shunt branch is given by:
I_{ 1 } = V_{ "in" } over { Z_{TL} }
and the current delivered by the source: I_{ "in" } = sqrt{P_{ "in" } over { Z_{TL} }} Thus, the current delivered to R1 and the load is I_{ 2 } = I_{ "in" } - I_{ 1 } .
Power dissipated by R1:
P_{ R1 } = P_{ R3 } = I_{ 2 }^2 ·R = P_{"in"} · { R·Z_{0} } over { (R + Z_{0})^2 }
Power delivered to the load:
P_{ "out" } = I_{ 2 }^2 · Z_{ 0 } = P_{"in"} · left( { Z_{0} over {R+Z_{0}} } right)^2
Sanity check:
P_{ "out" } = P_{ "in" } · left( { Z_{0} over {R+Z_{0}} } right)^2
%alpha = 10 · log_{10} left( {P_{"out"}}over{P_{"in"}}right) = 10·log_{10} left(left( { Z_{0} over {R+Z_{0}} } right)^2 right) = 20·log_{10} left( { Z_{0} over {R+Z_{0}} } right)
which matched the expression derived above from the S-parameters.

# L-pad - 1st series

## Design equations
I_{"in"} = I_{ shunt } + I_{"out"}
I_{ shunt } = V_{ out } over R_{ shunt } I_{ "in" } = -V_{ "in" } over Z_{ 0 } I_{ "out" } = V_{ "out" } over Z_{ 0 }
Replacing these three equations into the first one:
- {V_{"in"} over Z_0} = V_{ out } over R_{shunt}+ V_{"out"} over Z_0 dlrarrow -V_{"in"} over Z_0 = V_{ out } left ( 1 over R_{shunt} + 1 over Z_0 right ) = V_{ out } left ( {R_{shunt} · Z_0} over {R_{shunt} + Z_0} right )
Then, the voltage gain can be expressed as:
A_v = - {V_{ out } over V_{"in"}} = - {{ R_{shunt} } over { Z_0 + R_{shunt} }}
We are interested in the power attenuation so:
%alpha = P_{out} over P_{"in"} = {V_{out}^2 / Z_0} over {V_{"in"}^2 / Z_0} = A_v^2 = left( {{ R_{shunt} } over { Z_0 + R_{shunt} }} right )^2
Now, we must clear Rshunt from the previous equation and solve:
( 1 - %alpha) · R_{ shunt }^2 - 2 · %alpha ·Z_0 · R_{ shunt } - %alpha · Z_0 = 0
This equations yields two solutions for Rshunt:

Solution #1: R_{ shunt } = -{Z_0 · (%alpha + sqrt(%alpha))} over {%alpha - 1}
Solution #2: R_{ shunt } = -{Z_0 · (%alpha - sqrt(%alpha))} over {%alpha - 1}
Now, we must find the value of Rseries that satisfies the input match condition, i.e.:
Z_0 = R_{ series } + R_{shunt} parallel Z_{load} = R_{ series } + { R_{shunt} · Z_0 } over { R_{shunt} + Z_0 } drarrow R_{ series } = { Z_0^2 } over { Z_0 + R_{shunt} }
Then, for each one of the previous solution we find a Rseries value:
Solution #1: R_{ shunt } = -{Z_0 · (%alpha + sqrt(%alpha))} over {%alpha - 1} drarrow R_{ series } =-Z_0·{%alpha - 1} over {sqrt{%alpha} + 1}
Solution #2: R_{ shunt } = -{Z_0 · (%alpha - sqrt(%alpha))} over {%alpha - 1} drarrow R_{series} = Z_0·{%alpha - 1} over {sqrt{%alpha} - 1}
Notice that α is always less than 1.
Solution #1:
Rshunt is always positive and Rseries is also positive.
Solution #2:
Rshunt is always negative as α < sqrt(α)
Attenuation is usually expressed in dB, so:
%alpha^{ "dB)" } = 10 · log10( %alpha ) drarrow %alpha = 10^{ %alpha^{"db)"} / 10 }
The impedance seen by the load is:
Z_{ out } = R_{ shunt } parallel ( R_{series} + Z_0 ) = { R_{shunt} · (R_{series} + Z_0) } over { R_{shunt} + R_{series} + Z_0 }
## Power dissipation
The power dissipated by the series resistor is given by:
P_{ diss }^{ "ser" } = left( V_{"in"} - V_{"out"} right)^2 over R_{ series }
Since
V_{ "in" } = sqrt{ P_{"in"} · Z_0 } and V_{ "out" } = sqrt{ P_{"out"} · Z_0 } = sqrt{ P_{"in"} · %alpha · Z_0 }
P_{ diss }^{ "ser" } = left( V_{"in"} - V_{"out"} right)^2 over R_{ series } = { left( sqrt{P_{"in"} · Z_0} - sqrt{P_{"in"} · %alpha · Z_0} right)^2 } over R_{ series } = { P_{"in"} · Z_0 - 2 · sqrt{P_{"in"} · Z_0 · %alpha · P_{"in"} · Z_0} + P_{"in"} · Z_0 · %alpha} over R_{ series }
P_{ diss }^{ "ser" } = -(P_{"in"}·Z_0·%alpha + P_{"in"}·Z_0 - 2 · sqrt{P_{"in"} · Z_0 · %alpha} · sqrt{P_{"in"} · Z_0}) · {sqrt{%alpha} + 1} over {Z_0 · (%alpha - 1)}
P_{ diss }^{ "ser" } = P_{"in"} · ( 1 - sqrt(%alpha) )
With respect to the power dissipated by the shunt resistor, it is simply:
P_{ diss }^{ "sh" } = V_{"out"}^2 over R_{ shunt } = { P_{"in"} · %alpha · Z_0 } over R_{ shunt } = P_{ "in" } · %alpha · { 1 - %alpha } over { %alpha + sqrt{%alpha} }
# L-pad 1st shunt

## Design equations
{ V_{"in"} - V_{out} } over R_{ series } = V_{ out } over Z_0 drarrow V_{ out } over V_{ "in" } = Z_0 over { Z_0 + R_{series} }
A_v = Z_0 over { Z_0 + R_{series} } = sqrt{ %alpha } drarrow R_{ series } = { Z_0 · (1 - sqrt{%alpha}) } over sqrt{ %alpha }
The input port must be matched to Z0, so
Z_0 = R_{ shunt } parallel { R_{series} + Z_0 } = { R_{ shunt } · (R_{series} + Z_0 ) } over { R_{ shunt } + R_{series} + Z_0 } drarrow R_{ shunt } = { Z_0 · (R_{series} + Z_0) } over R_{ series} = Z_0 · 1 over { 1 - sqrt{%alpha} }
The output impedance is:
Z_out = R_{ series } + R_{ shunt } parallel Z_0 = -Z_0 · {%alpha - 2·sqrt(%alpha) + 2} over {%alpha - 2·sqrt(%alpha)}
## Power dissipation
P_{ shunt } = V_{ "in" }^2 over R_{ shunt } = V_{ "in" }^2 over R_{ shunt } = {P_{ "in" } · Z_0} over R_{ shunt } = {P_{ "in" } · Z_0} over left( Z_0 over {1 - sqrt{%alpha}} right) = P_{ "in" } · ( 1 - sqrt{%alpha} ) P_{ series } = left( V_{"in"} - V_{out} right)^2 over R_{ series } = left( sqrt{P_{"in"} · Z_0} - sqrt{P_{out} · Z_0} right)^2 over R_{ series } = left( sqrt{P_{"in"} · Z_0} - sqrt{P_{"in"} · %alpha · Z_0} right)^2 over R_{ series }
P_{ series } = {P_{"in"} · Z_0 - 2 · P_{"in"} · Z_0 · sqrt{%alpha} + P_{"in"} · %alpha · Z_0} over R_{ series } = P_{ "in" } · Z_0 · { 1 - 2 sqrt{%alpha} + %alpha } over R_{ series }
R_{ series } = { Z_0 · (1 - sqrt{%alpha}) } over sqrt{ %alpha } drarrow P_{ series } = P_{ "in" } · Z_0 · { 1 - 2 · sqrt{%alpha} + %alpha } over left( Z_0 · {1-sqrt{%alpha}} over {sqrt{%alpha}} right ) = P_{ "in" } · sqrt{ %alpha } · { 1 - 2 · sqrt{%alpha} + %alpha } over {1 - sqrt{%alpha}}
# Series resistor

## Design equation
Since the series resistor attenuator is unmatched, the design equations are derived more easily from the point of view of the reflection and transmission. There are two mismatch interfaces: the first one between the source and the series resistor and the second one between the series resistor and the load impedance.
In the first interface the attenuation is given by:
t_1 = 1 - left lline { Z_S - (R + Z_L) } over { Z_S + R + Z_L } right rline
In the second interface:
t_2 = 1 - left lline { (Z_S + R) - Z_L } over { Z_S + R + Z_L } right rline
Unless
So the total power loss is:
t = t_1 · t_2 = {4 · Z_L · Z_S} over {R^2 + 2·R·Z_L + Z_L^2 + 2·(R + Z_L) · Z_S + Z_S^2}
This gives two solutions, but only one gives positive values:
R_2 = (-(Z_L + Z_S) · %alpha + 2 · sqrt{Z_L · Z_S · %alpha}) over %alpha
## Power dissipation
The difference between the input and the output power is dissipated entirely by the series resistor.
P_{ diss } = P_{ "in" } - P_{ "out" } = P_{ "in" } · ( 1 - %alpha )
# Shunt resistor

## Design equation

As in the previous case, there are two mismatched interfaces: the first one between the source and shunt and the load in parallel and then the interface between the load and the shunt resistor and the source in parallel.
t_1 = 1 - left lline { Z_S - (R parallel Z_L) } over { Z_S + R parallel Z_L } right rline
t_2 = 1 - left lline { Z_S parallel R - Z_L } over { Z_S parallel R + Z_L } right rline
t = t_1 · t_2 = {4 · R^2 · Z_L · Z_S} over (R^2 · Z_L^2 + (R^2 + 2·R·Z_L + Z_L^2)·Z_S^2 + 2·(R^2·Z_L + R·Z_L^2)·Z_S)
This equation has two solutions, but just one gives positive values:
R = (2 · sqrt(Z_L · Z_S · %alpha) · Z_L · Z_S + (Z_L^2·Z_S + Z_L · Z_{S}^2)· %alpha) over(4 · Z_{L} · Z_{S} - (Z_L^2 + 2·Z_L·ZS + Z_S^2)· %alpha)
## Power dissipation
The difference between the input and the output power is dissipated entirely by the series resistor.
P_{ diss } = P_{ "in" } - P_{ "out" } = P_{ "in" } · ( 1 - %alpha )
# λ/4 lumped element equivalent circuits
It is possible to find lumped element impedance inverters that mimic the behaviour of a quarter-wavelength transmission line. The ABCD matrix of a generic transmission line is given by:
A_{ "TL" } = left[matrix{cosh(%gamma · l)# Z_{0}·sinh(%gamma · l)## {1} over {Z_{0}} ·sinh(%gamma · l) # cosh(%gamma · l) }right]
where %gamma = %alpha + j·%beta is the propagation constant, α is the attenuation coefficient and %beta = { 2·%pi } over { %lambda_{0} }
Under the assumption that the line is lossless, α = 0 → γ = j·β. Since the length of the line is one quarter of the wavelength at the operating frequency
A_{ "QW" } = left[matrix{0# j·Z_{0} ## {j} over {Z_{0}} # 0 }right]
## π type

The π network response is easily determined using the cascade property of the ABCD parameters. In this sense,

A_{ %pi } = A_{ "shunt1" } · A_{ "series" } · A_{ "shunt2" } where
A_{ "shunt1" } = left[matrix{1# 0 ## Y_{1} # 1}right] A_{ "series" } = left[matrix{1# Z_{1} ## 0 # 1}right] A_{ "shunt2" } = left[matrix{1# 0 ## Y_{2} # 1}right]
A_{ %pi } = left[matrix{Y_{2}·Z_{1} + 1 # Z_{1} ## (Y_{1} · Z_{1} + 1)·Y_{2} + Y_{1} # Y_{1}·Z_{1} + 1}right]
A_{ %pi } = A_{ QW } dlrarrow left lbrace matrix{Y_{2}·Z_{1} + 1 = 0 ## Z_{1} = j·Z_{0} ## (Y_{1}·Z_{1} + 1)·Y_{2} + Y_{1} = j over Z_{0} ## Y_{1}·Z_{1} +1 =0} right rbrace

From the second equation, Z1 must be an inductor: Z1 = j·ω0·L = j·Z0 → L = Z0/ω0
From the first and the fourth equations, Y1 = Y2
Y_{ 1 } · j·Z_{ 0 } + 1 = 0 dlrarrow Y_{ 1 } = Y_{2} = -1 over { j·Z_{0} } = j over { Z_{0} }
So the shunt elements must be capacitors such as:
Y_{ 1 } = Y_{ 2 } = j·%omega_0 · C = j over Z_{ 0 } drarrow C = 1 over {%omega_{0} · Z_{0}}
Finally, substituiting Y1, Y2 and Z1 in the third equation, we get:
(Y_{1}·Z_{1} + 1)·Y_{2} + Y_{1} = j over Z_{0} dlrarrow ( {j over Z_{0}} · j·Z_{0} + 1)· { j over Z_{0} } + { j over Z_{0} } = { j over Z_{0} } dlarrow ( -1 + 1 ) · { j over Z_{0} } = { j over Z_{0} }
So the values L and C calculated above make a CLC π network to match the ABCD parameters of a quarter wavelength transmission line at ω0
## Tee type

A_{ "tee" } = A_{ "series1" } · A_{ "shunt" } · A_{ "series2" } where
A_{ "series1" } = left[matrix{1# Z_{1} ## 0 # 1}right] A_{ "shunt" } = left[matrix{1# 0 ## Y_{1} # 1}right] A_{ "series2" } = left[matrix{1# Z_{2} ## 0 # 1}right]
A_{ "tee" } = left[matrix{Y_{1}·Z_{2} + 1# Y_{1} ## (Y_{1}·Z_{1} + 1)·Z_{2} + Z_{1} # Y_{1}·Z_{1}+1}right]
A_{ "tee" } = A_{ QW } dlrarrow left lbrace matrix{Y_{1}·Z_{2} + 1 = 0 ## Y_{1} = j·Z_{0} ## (Y_{1}·Z_{1} + 1)·Z_{2} + Z_{1} = j over Z_{0} ## Y_{1}·Z_{1} +1 =0} right rbrace
From the second equation, Y1 must be an capacitor: Y1 = j·ω0·C = j·Z0 → C = Z0/ω0
From the first and the fourth equations, Z1 = Z2
j·Z_{0} · Z_{ 1 } + 1 = 0 dlrarrow Z_{ 1 } = Z_{2} = -1 over { j·Z_{0} } = j over { Z_{0} }

So the series elements must be inductors such as:
Z_{ 1 } = Z_{ 2 } = j·%omega_0 · L = j over Z_{ 0 } drarrow L = 1 over {%omega_{0} · Z_{0}}
Finally, substituiting Z1, Z2 and Y1 in the third equation, we get:
(Y_{1}·Z_{1} + 1)·Z_{2} + Z_{1} = j over Z_{0} dlrarrow (j·Z_{0}·{j over Z_{0}} + 1)·{j over Z_{0}} + {j over Z_{0}} = j over Z_{0} dlrarrow {j over Z_{0}} = j over Z_{0}
So the values L and C calculated above make a CLC π network to match the ABCD parameters of a quarter wavelength transmission line at ω0
# Power unit conversion
## Conversion from W to dBm
P[ dBm ] = 10 · log_{ 10 } left( P[W] · 10^{-3} right ) = 10 · log_{ 10 } left( P[W] right ) - 30
P[ W ] = 10^{0.1 · P [ dBm ]} + 30
## Conversion from dBm to dBuV and dBmV

P [W] = { (V [V])^2} over { Z_{0} [%OMEGA] } = { (V [%mu V] · 10^6)^2} over { Z_{0} [%OMEGA] } drarrow P^{ "dB"%mu"V" } = 20·log_{ 10 } ( sqrt{P[W] · Z_{0}[%OMEGA]}) + 20 · log_{ 10 } ( 10^6 )
P^{ "dBuV" } = 10·log_{ 10 } ( P[W] · Z_{0}[%OMEGA]) + 120 = 10·log_{ 10 } ( P[W] ) + 10·log_{10} (Z_{0}[%OMEGA]) + 120
P[W] = 10^{0.1 · (P^{ "dBuV" } - 120 - 10·log_{10} (Z_{0}[%OMEGA]))}

Similarly, for the dBmV case:
P [W] = { (V [V])^2} over { Z_{0} [%OMEGA] } = { (V [m V] · 10^3)^2} over { Z_{0} [%OMEGA] } drarrow P^{ "dBmV" } = 20·log_{ 10 } ( sqrt{P[W] · Z_{0}[%OMEGA]}) + 20 · log_{ 10 } ( 10^3 )
P^{ "dBmV" } = 10·log_{ 10 } ( P[W] · Z_{0}[%OMEGA]) + 60 = 10·log_{ 10 } ( P[W] ) + 10·log_{10} (Z_{0}[%OMEGA]) + 60
P[W] = 10^{0.1 · (P^{ "dBmV" } - 60 - 10·log_{10} (Z_{0}[%OMEGA]))}

## Summary table

from \ to	W	dBm	dBuV[75Ω]	dBmV[75Ω]	dBuV[50Ω]	dBmV[50Ω]
W		10 · log_{ 10 } ( P^W ) + 30	10·log_{ 10 } ( P^W ) + 138.75	10·log_{ 10 } ( P^W ) + 78.75	10·log_{ 10 } ( P^W ) + 136.99	10·log_{ 10 } ( P^W ) + 76.99
dBm	10^{0.1 · P^{ dBm }} + 30		P^{ "dBm" } + 108.75	P^{ "dBm" } + 48.75	P^{ "dBm" } + 106.99	P^{ "dBm" } + 46.99
dBuV[75Ω]	10^{0.1 · (P^{ "dB"%mu"V" } - 138.75)}	P^{ "dB"%mu"V" } - 108,75		P^{ "dB"%mu"V" } - 60	P^{ "dB"%mu"V" } - 1,76	P^{ "dB"%mu"V" } - 61,76
dBmV[75Ω]	10^{0.1 · (P^{ "dBmV" } - 78.75)}	P^{ "dBmV" } - 48.75	P^{ "dBmV" } + 60		P^{ "dBmV" } + 58,35	P^{ "dBmV" } - 1,76
dBuV[50Ω]	10^{0.1 · (P^{ "dB"%mu"V" } - 136.99)}	P^{ "dB"%mu "V" } - 106.99	P^{ "dB"%mu"V" } + 1,76	P^{ "dB"%mu"V" } - 58,35		P^{ "dB"%mu"V" } - 60
dBmV[50Ω]	10^{0.1 · (P^{ "dBmV" } - 76.99)}	P^{ "dBmV" } - 46.99	P^{ "dBmV" } + 61,76	P^{ "dBmV" } + 1,76	P^{ "dBmV" } + 60

# References
[1] RF design guide. Systems, circuits, and equations. Peter Vizmuller. Artech House, 1995
[2] The PIN diode circuit designer's handbook. W.E. Doherty, Jr., R.D. Joos, Microsemi Corp., 1998

# Files
The following files should be enclosed with this document:
- After_vs_before.sch: Shows how the aspect of the circuits changed in this pull request. Basically, it was added some extra space between the components.
- BridgedTee_w_wo_SP_block.sch: Includes a 15dB bridged-tee attenuator with and without the S-parameter option activated.
Similar files: Pi_Att_w_wo_SP_block.sch, Tee_Att_w_wo_SP_block.sch
- Bridged_Tee_PowerDissipation.sch: It calculates the power dissipated by each resistor using the AC simulation. It is useful to check the results given by the power dissipation calculator included in the GUI.
  Similar files: Pi_Tee_PowerDissipation.sch, Quarter-Wave-Attenuator-Series-Power-Dissipation.sch, Quarter-Wave-Attenuator-Shunt-Power-Dissipation.sch and Reflection_Attenuator_Power_Dissipation.sch
- Bridged_Tee_Power_Dissipation_Curves.sch: It calculates the power dissipated by each resistor versus attenuation using the AC analysis.
  Similar files: Pi_Tee_Power_Dissipation_Curves.sch, Quarter-Wave-Attenuator-Series-Power-Dissipation-Curves.sch
- Pi_Tee_Attenuator.m: Calculates the minumum achievable attenuation with a π/tee-type attenuator and the relative power dissipated by each resistor wrt the input power.
  Similar files: Bridged_Tee_Attenuator.m, QW_Series_Attenuator.m and Reflection_Attenuator.m